Z80 Home Brew #3
Monitor ROM
December 11, 2022

## Overview
The monitor may be entered from a running program by pressing the NMI button or by executing a RST 1 instruction (0xCF) in the program. In the case of RST 1, the saved PC will point to the RST 1 instruction (not the next instruction). In both cases, the saved PC is printed after a ‘>’ character before entering the monitor loop.

Pressing NMI while running the monitor is similar to RESET.
## Implemented Commands
In the following, addr and byte are entered in hexadecimal. [ ] means the parameter is optional. CR means the carriage return key.

[addr]CR
print the byte stored at addr, advance addr by 1.

[addr]/
print the word stored at addr, advance addr by 2. Also used after T or R commands to view subsequent values/

[addr]I
Input bytes starting at addr. Prints address and current contents and waits for input. Commands are:
[byte]CR
store byte (if entered) in addr, increment addr by 1.
-
decrement addr by 1.
.
return to monitor

[addr]G
Go (start execution) at addr or saved PC

P
start execution at PC+1 (for continuing after RST 1 traps).

T
print word at saved SP (top of stack), increment addr by 2. The top of stack will not include the PC that was pushed as part of the NMI or RST 1. The rest of the stack may be viewed by using / commands.

Rreg/
print contents of saved register pair. reg is one of: A,B,D,H,A',B',D',H',X,Y,S,P. Increment addr by 2, effectively selecting the next register pair.
## Unknown Commands
^
“up”?

V
“down”?

H
Host control mode?
## Host Control Commands
x