Z80 Home Brew #3
Monitor ROM
December 12, 2022

## Overview
The machine consists of a Z80-CPU, 2K EPROM (expandable to 4K), 4K of RAM, two Z80-PIO, one Z80CTC, one Z80-SIO/0, and an HDSP-2111 8-character 5x7 LED dot matrix display. All four PIO channels are wired to a 50-pin FCC connector (P3). Both SIO channels are wired to a DIP14 socket/connector (P4). General-purpose I/O expansion is provided on a pair of DIP14 sockets/connectors (P1, P2). The HDSP-2111 display is wired as an I/O expansion.

The original EPROM for this machine was damaged, and all odd pages (256-byte chunks) are missing (A8 shorted to GND). Half the monitor code is missing, but some things can be reconstructed or restored based how the existing code interacts.
## General Operation
The monitor may be entered from a running program by pressing the NMI button or by executing a RST 1 instruction (0xCF) in the program. In the case of RST 1, the saved PC will point to the RST 1 instruction (not the next instruction). In both cases, the saved PC is printed after a ‘>’ character before entering the monitor loop.

Pressing NMI while running the monitor is similar to RESET.

The monitor prompt is the asterisk (‘*’) character, however that is reconstructed code and there is no indication what the prompt character was originally.
## User Commands
In the following, addr and byte are entered in hexadecimal. [ ] means the parameter is optional. CR means the carriage return key. LF means the line feed key.
### Implemented Commands
The following commands either have code that defines the operation, or can be reasonably determined based on space available and logical deduction.

[addr]CR
print the byte stored at addr, advance addr by 1.

[addr]/
print the word stored at addr, advance addr by 2. Also used after ‘T’ or ‘R’ commands to view subsequent values.

[addr]I
Input bytes starting at addr. Prints current address and current contents and waits for input. Commands are:
[byte]CR
store byte (if entered) in addr, increment addr by 1. CR alone is used to skip to next location without altering contents.
-
decrement addr by 1.
.
return to monitor

[addr]G
Go (start execution) at addr or saved PC

P
start execution at PC+1 (for continuing after RST 1 traps).

T
print word at saved SP (top of stack), increment addr by 2. The top of stack will not include the PC that was pushed as part of the NMI or RST 1. The rest of the stack may be viewed by using ‘/’ commands.

Rreg/
print contents of saved register pair. reg is one of: A,B,D,H,A',B',D',H',X,Y,S,P. Increment addr by 2, effectively selecting the next register pair. Successive registers may be viewed by using ‘/’ commands.
H
Host control mode? Appears to accept commands from SIO channel B, as if connected to a remote computer. Remote commands are echoed to console (channel A), unclear what other interaction there is. Or possibly just an alternate set of commands still using the console.

### Unknown Commands
The following commands do not have code.

LF
(unknown)

^
“up”?

V
“down”?

## Host Control Commands
Host control commands may be prefixed with an octal number. Unclear how data is sent back to host (in octal?). Might still be controlled by console, unclear if any interaction with host.

.
(unknown)

,
(unknown)

\
(unknown)

LF
(unknown)

CR
(unknown)

S
(unknown)

R
(unknown)

X
Exit Host mode, return to monitor

M
(unknown interaction with PIO-connected device)

/
(unknown)

^
(unknown)

<
(unknown)

>
(unknown)

G
Get 2K bytes from PIO-connected device. Read pairs of 4-bits from PIO2A. Buffer at 1600H.

P
Put 2K bytes to PIO-connected device. Writes pairs of 4-bits to PIO2B. Buffer at 1600H.

TBD
enter Terminal mode, with HEX loading enabled.

[addr]TBD
Write addr to the PIO-connected device as two 6-bit values on pio1A, strobing pio2B bit 4 for low character and pio2B bit 5 for high character. The value addr is first decremented by 2 and xor’ed with 1. Any bits beyond the 12 are ignored.

## Terminal Mode Operation
The code passes characters both directions between SIO channels A and B. In addition, there is a mode where the stream coming from channel B may contain Intel HEX format data, which is presumably loaded into memory. The console (channel A) user may press Ctrl-] (0x1d, ASCII “GS”) to cause a BREAK condition to be sent to channel B, presumably to disconnect from the host or terminate a program. There is some number of successive Ctrl-] presses required to activate the BREAK feature, to avoid accidental disconnect. At least one other key command seems to exist, possibly to exit terminal mode. Considering the nature of “terminal mode”, this exit key would have been some control character that is not normally used (similar to the BREAK code).